## Slide 1: From Frame to Forward
Building a small office network with internet access
Data link layer > Network layer > Internet
Notes: Introduce the project: we design a small LAN for one company floor and follow data from Ethernet frames up to IP routing and NAT.

## Slide 2: What we are building
THE SCENARIO
One company floor. Everyone shares a printer and reaches the internet through one router.
1
Router
Connects the office to the internet
2
Switches
Connect the wired devices
4
Employee PCs
Wired desktops
1
Printer
Shared by everyone
1
Wi-Fi access point
Creates the wireless network
2
Wireless devices
A laptop and a phone

## Slide 3: How everything is connected
NETWORK DIAGRAM
WIRED LAN 192.168.10.0/26
WIRELESS LAN 192.168.10.64/26
Internet
Router
WAN 203.0.113.10
Switch 1
Switch 2
Access point
PC1
.10
PC2
.11
Printer
.5
PC3
.12
PC4
.13
Laptop
.70
Phone
.71
Solid line = Ethernet cable Dashed orange = Wi-Fi radio
Notes: The router has three ports: G0/0 to the internet (ISP), G0/1 to Switch 1 (wired subnet), G0/2 to the access point (wireless subnet). Switch 2 hangs off Switch 1.

## Slide 4: MAC addresses & frames
01
Who is who on the local network, what a frame looks like, and how collisions are handled.

## Slide 5: Every device gets a MAC address
PART 1 · MAC ADDRESSES
Device | MAC address | Connected to
Router - port G0/0 (internet) | 00:1A:2B:10:00:01 | ISP
Router - port G0/1 (wired) | 00:1A:2B:10:00:02 | Switch 1
Router - port G0/2 (wireless) | 00:1A:2B:10:00:03 | Access point
Switch 1 | 00:1A:2B:20:00:01 | Router
Switch 2 | 00:1A:2B:20:00:02 | Switch 1
PC1 | 00:1A:2B:30:00:01 | Switch 1
PC2 | 00:1A:2B:30:00:02 | Switch 1
PC3 | 00:1A:2B:30:00:03 | Switch 2
PC4 | 00:1A:2B:30:00:04 | Switch 2
Printer | 00:1A:2B:40:00:01 | Switch 1
Wi-Fi access point | 00:1A:2B:50:00:01 | Router
Laptop (wireless) | 00:1A:2B:60:00:01 | Access point
Phone (wireless) | 00:1A:2B:60:00:02 | Access point
Reading a MAC
00:1A:2B : 30:00:01
First half = maker (OUI)
Second half = this device
48 bits, written as 12 hex digits. Burned into the network card and works only inside the local network.
The second byte of the device part shows the type: 10 router, 20 switch, 30 PC, 40 printer, 50 AP, 60 wireless.
Notes: Real MACs are set by the manufacturer; we use a readable numbering scheme so the documentation is easy to follow. A router has one MAC per port.

## Slide 6: A frame from PC1 to the printer
PART 1 · FRAME STRUCTURE
Preamble
7 bytes
1010... sync
SFD
1 byte
Start of frame
Destination MAC
6 bytes
00:1A:2B:40:00:01
(Printer)
Source MAC
6 bytes
00:1A:2B:30:00:01
(PC1)
Type
2 bytes
0x0800
= IPv4
Payload (data)
46 - 1500 bytes
IP packet:
192.168.10.10 to .5
+ the print job
FCS
4 bytes
CRC error
check
Start signal
Header (14 bytes)
Data
Trailer
1. Before sending: ARP
PC1 knows the printer's IP but not its MAC. It broadcasts "Who has 192.168.10.5?" and the printer replies with its MAC.
2. At the switch
The switch reads only the destination MAC, checks its MAC table and sends the frame out of the printer's port only.
3. At the printer
The printer recalculates the FCS. If it matches, the frame is good and the data goes up to IP. If not, it is dropped.
Notes: PC1 and the printer are in the same subnet, so the frame goes straight through the switch. The router is not involved.

## Slide 7: Who talks first? Wired vs. wireless
PART 1 · COLLISIONS
Ethernet (wired)
CSMA/CD - detect collisions
Old hubs put everyone on one shared wire, so two PCs could send at once and collide.
CSMA/CD: listen first. If a collision is detected, stop, wait a random time, retry.
Our switches give each device its own port in full-duplex: it can send and receive at the same time.
Each switch port = its own collision domain, so collisions basically never happen.
Wi-Fi (wireless)
CSMA/CA - avoid collisions
A radio cannot listen while it sends, so collisions cannot be detected. They must be avoided.
CSMA/CA: listen. If the air is busy, wait a random backoff time, then send.
The receiver answers with an ACK. No ACK = send again. RTS/CTS can reserve the air for hidden devices.
Listen > Wait random time > Send > Get ACK

## Slide 8: IP addressing & subnetting
02
Pick a private range, split it into wired and wireless, and let DHCP hand out addresses.

## Slide 9: One /24 split into two working subnets
PART 2 · SUBNETTING
Private range 192.168.10.0/24 = 256 addresses. We cut it into four /26 blocks of 64 and use two of them.
Wired
192.168.10.0 - .63
Wireless
192.168.10.64 - .127
Spare
192.168.10.128 - .191
Spare
192.168.10.192 - .255
Wired subnet
Network | 192.168.10.0/26
Mask | 255.255.255.192
Usable hosts | .1 to .62 (62 hosts)
Broadcast | 192.168.10.63
Default gateway | 192.168.10.1 (router G0/1)
Wireless subnet
Network | 192.168.10.64/26
Mask | 255.255.255.192
Usable hosts | .65 to .126 (62 hosts)
Broadcast | 192.168.10.127
Default gateway | 192.168.10.65 (router G0/2)
Why split? Wi-Fi guests and phones stay apart from wired PCs and the printer, broadcasts stay small, and the two spare blocks leave room to grow.

## Slide 10: IP address for every device
PART 2 · IP PLAN
Device | Subnet | IP address | Default gateway | Assigned by
Router G0/1 (wired side) | Wired | 192.168.10.1 | - | Static
Router G0/2 (wireless side) | Wireless | 192.168.10.65 | - | Static
Router G0/0 (internet side) | Public | 203.0.113.10 | 203.0.113.1 (ISP) | From ISP
Switch 1 (management) | Wired | 192.168.10.2 | 192.168.10.1 | Static
Switch 2 (management) | Wired | 192.168.10.3 | 192.168.10.1 | Static
Printer | Wired | 192.168.10.5 | 192.168.10.1 | Static
PC1 / PC2 | Wired | 192.168.10.10 / .11 | 192.168.10.1 | DHCP
PC3 / PC4 | Wired | 192.168.10.12 / .13 | 192.168.10.1 | DHCP
Wi-Fi access point | Wireless | 192.168.10.66 | 192.168.10.65 | Static
Laptop | Wireless | 192.168.10.70 | 192.168.10.65 | DHCP
Phone | Wireless | 192.168.10.71 | 192.168.10.65 | DHCP
Mask for every LAN device: 255.255.255.192 (/26). Default gateway = the router port on the same subnet: the door out of the local network.

## Slide 11: DHCP: automatic addresses in four messages
PART 2 · DHCP
New device
e.g. the laptop
DHCP server
the router
1 Discover "Is there a DHCP server here?" (broadcast)
2 Offer "You can use 192.168.10.70"
3 Request "Great, I'll take .70"
4 Acknowledge "It's yours, with gateway and DNS"
The device receives
IP address
Subnet mask
Default gateway
DNS server
Lease time
Our two pools
Wired: .10 to .50
Wireless: .70 to .120
Router, switches, printer and AP keep static IPs so they never move.
Notes: DORA: Discover, Offer, Request, Acknowledge. Without DHCP, every new phone or laptop would need its IP typed in by hand. The printer is static so print jobs always find it.

## Slide 12: Routing & packet forwarding
03
Follow the laptop as it opens www.example.com: from Wi-Fi, through the router and NAT, to the internet and back.

## Slide 13: Laptop to website: the path at a glance
PART 3 · THE PATH
Wi-Fi
Laptop
192.168.10.70
Ethernet
Access point
bridges Wi-Fi
ISP link
Our router
routing + NAT
hops
ISP router
203.0.113.1
hops
Internet
many routers
Web server
93.184.216.34
Never changes
Destination IP 93.184.216.34. Every router reads it to choose the way forward.
Changes once (at our router)
Source IP: 192.168.10.70 becomes 203.0.113.10 because of NAT.
Changes at every hop
MAC addresses (a new frame for each link) and TTL, which drops by 1.

## Slide 14: What happens when the laptop opens a website
PART 3 · STEP BY STEP
1
Find the IP (DNS)
The laptop asks DNS: "What is the IP of www.example.com?" Answer: 93.184.216.34.
2
Local or remote?
Using its mask, the laptop sees 93.184.216.34 is not in 192.168.10.64/26. So it sends to its gateway, 192.168.10.65.
3
Get the gateway's MAC (ARP)
"Who has 192.168.10.65?" The router answers with port G0/2's MAC 00:1A:2B:10:00:03.
4
Over the air to the AP
The laptop sends a Wi-Fi frame (CSMA/CA). The access point passes it on to the router as an Ethernet frame.
5
At the router
It removes the frame, reads the IP header, lowers TTL, picks the next hop, applies NAT and builds a new frame for the ISP.
6
Across the internet and back
Each router repeats "read IP, pick next hop". The reply comes back to 203.0.113.10 and NAT sends it to the laptop.

## Slide 15: How routers use the IP header
PART 3 · THE IP HEADER
Version 4
Header length
Type of service
Total length
Identification
Flags
Fragment offset
TTL 64
Protocol 6 = TCP
Header checksum
Source IP 192.168.10.70
Destination IP 93.184.216.34
Highlighted = fields the router reads or changes
1
Destination IP
Looked up in the routing table to choose the next hop.
2
TTL
Lowered by 1 at every router. At 0 the packet is dropped, so it can never loop forever.
3
Checksum
Recalculated, because TTL (and NAT) changed the header.
4
Source IP
Rewritten by NAT at our router so replies can find their way back.

## Slide 16: How the router decides the next hop
PART 3 · NEXT HOP
Destination network | Next hop | Exit port | Meaning
192.168.10.0/26 | Directly connected | G0/1 | Wired LAN
192.168.10.64/26 | Directly connected | G0/2 | Wireless LAN
0.0.0.0/0 (default route) | 203.0.113.1 (ISP) | G0/0 | Everything else = internet
Our router's routing table
Looking up 93.184.216.34
192.168.10.0/26?
No
192.168.10.64/26?
No
0.0.0.0/0?
Yes - matches all
Result: send it to 203.0.113.1 out of port G0/0.
The rule
If several routes match, the most specific one (longest mask) wins. The default route /0 is the last resort.

## Slide 17: NAT: the whole office shares one public IP
PART 3 · NAT
Inside (private) - before NAT
Source: 192.168.10.70 : 51000
Destination: 93.184.216.34 : 443
Outside (public) - after NAT
Source: 203.0.113.10 : 40001
Destination: 93.184.216.34 : 443
Router rewrites the source
NAT table kept by the router
Device | Inside address | Outside address
Laptop | 192.168.10.70 : 51000 | 203.0.113.10 : 40001
Phone | 192.168.10.71 : 52000 | 203.0.113.10 : 40002
On the way back: the reply arrives for 203.0.113.10 : 40001. The router looks it up, swaps it back to 192.168.10.70 : 51000 and forwards it to the laptop.
Why NAT?
Private IPs (192.168.x.x) are not allowed on the internet.
Every office device shares one public IP from the ISP.
Inside addresses stay hidden from the outside.
Notes: This is PAT (port address translation), the most common form of NAT. The port number tells the router which inside device a reply belongs to.

## Slide 18
Key takeaways
MAC & frames
MAC addresses deliver frames inside the LAN. Switches remove collisions; Wi-Fi avoids them with CSMA/CA.
IP & subnets
192.168.10.0/24 split into wired /26 and wireless /26. DHCP hands out addresses automatically.
Routing & NAT
Routers read the destination IP to pick the next hop. NAT lets every device share one public IP.
Frame inside the LAN, packet across the internet.